November 2014

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5617 BA Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Robert Bosch (SEA) Pte Ltd, Security Systems 11 Bishan Street 21 Singapore 573943 Phone: +65 6571 2808 Fax: +65 6571 2699 apr.securitysystems@bosch.com www.boschsecurity.asia |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 29

VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

BOSCH VKC-5085 DINION D/N Camera Kit

- – GENERAL

  - SUMMARY

    - Section Includes

      - Video Surveillance Remote Devices.

    - Related Sections

      - Section [28 23 13 – Video Surveillance Control and Management Systems].

      - Section [28 23 16 – Video Surveillance Monitoring and Supervisory Interfaces].

      - Section [28 23 19 – Digital Video Recorders and Analog Recording Devices].

      - Section [28 23 23 – Video Surveillance Systems Infrastructure].

**********Specifier’s note: Include those standards referenced elsewhere in this SECTION.

  - REFERENCES

| Standards |
| --- |
|  | FCC Part15 Subpart B, Class B |
|  | EN 55022 class B |
|  | EN61000-3-2 |
|  | EN61000-3-3, |
|  | EN 50130-4 |
|  | EN 50121-4 |
|  | Camera with 500 g (1.1 lbs) lens according to IEC 60068-2-6 |
| VKN-5085V4-20; VKN-5085V10-20 | EN60950-1, UL60950-1 (2ND edition), CSA C22.2 No. 60950-1-07 (2ND edition) |
| VKN-5085V4-50; VKN-5085V10-50 | EN60950-1 |

| Product certifications | CE, FCC, UL, CSA |
| --- | --- |

  - DEFINITIONS

    - Day/Night (infrared sensitive): A camera that has normal color operation in situations where there is sufficient illumination (day conditions), but where the sensitivity can be increased when there is little light available (night conditions). This is achieved by removing the infrared cut filter required for good color rendition. The sensitivity can be further enhanced by integrating a number of fields to improve the signal-to-noise ratio of the camera (this may introduce motion blur).

    - Privacy Masking: The ability to mask out a specific area to prevent it from being viewed in order to comply with privacy laws and particular site requirements.

    - SensUp (sensitivity up): Increases camera sensitivity by increasing the integration time on the CCD (lowering shutter time from 1/50s to 1/5 s – PAL; 1/60s to 1/6s - NTSC). This is accomplished by integrating the signal from a number of consecutive video fields to reduce signal noise.

    - Smart BLC (Back Light Compensation): Smart back-light compensation allows the camera to automatically compensate for bright areas of a high contrast scene without having to define a window or area.

  - SYSTEM DESCRIPTION

    - Video Surveillance Remote Devices

      - VKN-5085 Series Dinion HDR Day/Night Camera Kit

    - Performance Requirements

      - Stylish and sturdy housing (IP66; NEMA 4x)

      - 1/3-inch 960H CCD sensor with High Dynamic Range.

      - 720TVL sensor resolution.

      - Dynamic engine with Smart BLC.

      - True Day/Night performance with switchable filter.

      - Bilinx communication for remote set-up and control.

      - Six independent, pre-programmed operating modes.

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00].

    - Product Data:

      - Manufacturer’s data, user and installation manuals for all equipment and software programs including computer equipment and other equipment required for complete video management system.

    - Shop Drawings; include

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals

      - User manual.

      - Parts list.

      - System device locations on architectural floor plans.

      - Wiring and connection diagram.

      - Maintenance requirements.

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design Video Surveillance Devices.

      - Manufacturer’s quality system: Registered to ISO 9001 Quality Standard.

    - Video Surveillance System

      - Listed by [UL] [EN] [FCC] specifically for the required loads.  Provide evidence of compliance upon request.

    - Installer:

      - Minimum of [5] years experience installing Video IP Surveillance System.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section [01 60 00].

    - Deliver materials in manufacture’s original, unopened, undamaged containers; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions.

    - Bosch provides off-the-shelf availability for our top selling products and same-day or 24-hour shipping.

  - WARRANTY

    - Provide manufacturer’s warranty covering [3] years for replacement and repair of defective equipment.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m. via phone and e-mail.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5617 BA Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

[Robert Bosch (SEA) Pte Ltd, Security Systems

11 Bishan Street 21

Singapore 573943

Phone: +65 6571 2808

Fax: +65 6571 2699

apr.securitysystems@bosch.com

www.boschsecurity.asia]

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

**********Specifier’s note: Select Camera System Series based on project requirement.

  - BOSCH VKN-5085 SERIES DINION HDR DAY/NIGHT CAMERA KIT [VKN-5085-V4-50] [VKN-5085-V10-50] [VKN-5085-V4-20] [VKN-5085-V10-20]

    - General Characteristics:

      - The product specified shall be a prepackaged camera and lens built into a housing designed for indoor/outdoor operation.

      - The camera housing shall be constructed of an aluminum casing, neoprene gaskets, UV-resistant polymer end caps, and all stainless steel hardware. The viewing window shall be 3 mm (0.12 in.) thick glass.

      - The housing kit shall be equipped with a heater, blower, and sunshield to protect against environmental extremes.

      - A compatible feed-through wall mount shall be provided by the manufacturer to support a maximum load of 20 lbs (9 kg). The mount shall have a swivel head that rotates 360º and tilts 180º. To ensure neatness of installation, the mount shall be designed to allow feed through wiring.

      - The kit shall meet IP66 and NEMA-4X enclosure protection standards.

      - The prepackaged camera shall utilize 1/3-inch day/night CCD image sensor capable of 720TVL sensor resolution.

      - The camera shall provide six distinct pre-programmed operational modes stored in the camera.

      - The camera shall provide a video motion detection function that provides four fully programmable areas.

      - The camera shall provide fifteen independent, fully programmable privacy mask areas.

      - The camera shall produce a composite video signal, via a BNC connector, that allows a direct input to a conventional analog matrix switcher, DVR, or any standard analog CCTV video equipment.

      - The camera shall provide an on-screen display to simplify the camera/lens back focus and network configuration settings.

      - The camera shall accept CS-mount type and C-mount type lenses.

      - The camera shall provide a lens wizard during lens back focus setup to allow focusing at maximum lens opening to ensure that the object of interest within the field of view always remains in focus.

      - The camera shall provide a frame integration mode (Bosch SensUp feature) that can produce a color image with a minimum scene illumination of 0.009 lux (0.000837fc) under 50IRE and a monochrome image, when in the night mode, with a minimum illumination of 0.004 lux (0.000372fc) under 50IRE.

      - The camera shall provide a feature (SensUP) that enhances camera sensitivity by increasing the integration time on the CCD (lowering shutter time from 1/50 s to 1/5 s – PAL; 1/60 s to 1/6 s - NTSC). This is accomplished by integrating the signal from a number of consecutive video fields to reduce signal noise.

      - The camera shall provide enhanced night viewing through the increase of IR sensitivity by automatically switching a motorized IR filter from color to monochrome operation in low-light or IR illuminated applications. Allow the IR filter to be switched manually via the alarm input, preprogrammed in a camera mode or profile.

      - The camera shall utilize XF-Dynamic technology to extend the dynamic range of the camera to provide a sharper image, simultaneously, in both the high-light and low-light areas of the scene.

      - The camera shall utilize HDR technology to extend the dynamic range of the camera to provide a sharper, more detailed image for increased accuracy in color reproduction in harsh lighting conditions.

      - The camera shall utilize Smart BLC technology to automatically compensate the image without compromising dynamic range.

      - The camera shall utilize Peak White Invert technology to reduce glare from highlight area.

      - The camera shall provide Bilinx feature to allow user to check status, change camera settings and update firmware from virtually anywhere along the video cable.

      - The camera shall provide E-zoom with the zoom rate up to 16.

    - Installation Requirements

      - The camera shall provide a built-in test pattern generator.

      - The camera kit shall be easy to install.

      - The camera shall provide a multi-language on-screen display.

      - The camera kit shall provide cable compensation which can extend transmission distance up to 1000m without external amplifiers.

    - Alarm Handling Features:

      - The camera shall provide an alarm input that may be triggered by either a normally opened or normally closed contact.

      - The camera shall provide the capability on alarm to display up to a 17 character, programmable alarm message.

      - The camera shall provide a relay output that may be selected for normally opened or normally closed operation. The relay can be activated from an external alarm input to the camera, upon video motion detection, or when camera shifting to monochrome mode.

    - Electrical

      - The housing shall accept 24 VAC [VKC-5085V4-20, VKC-5085V10-20] or 230 VAC [VKC-5085V4-50, VKC-5085V10-50].

      - The camera shall accept either 12 VDC or 24 VAC.

      - The kit shall consume 45 W (max.).

    - Pre-wired

      - The kits shall be available with the following wiring options:

        - Pre-wired with a power and BNC cable fed through the foot of the housing [VKC-5085V4-20, VKC-5085V10-20] 
The 3-conductor power cable shall be terminated with flying leads.

        - No wiring [VKC-5085V4-50, VKC-5085V10-50] but with cable installation components supplied.

    - Lens

      - The pre-packaged cameras shall be available with a choice of factory installed super resolution megapixel lens:

        - 5.0-50 mm varifocal lens [VKC-5085V4-20, VKC-5085V4-50]

        - 2.8-12 mm varifocal lens [VKC-5085V10-20, VKC-5085V10-50]

    - Environmental

      - The housing kit shall operate in -40°C to +50°C (-40°F to +122°F) temperature range, and can be stored in -40°C to +70°C (-40°F to +158°F) range.

    - Technical specifications:

| Mechanical Housing |
| --- |
| Dimensions (H x W x L) - closed and including sunshield | 126.5 x 171.3 x 480 mm (5 x 6.7 x 18.9 in.) |
| Weight (including camera and lens) | 3.9 kg (8.6 lbs) |
| Construction | Aluminum casing, neoprene gaskets, all stainless steel hardware, 3.3 mm (1/8 in.) thick glass window |
| Color | Gray |
| Locking clasps (3x) | Tamper-resistant screws provided |
| Camera mounting | Removable camera/lens tray, mounted with two screws |
| Max camera + lens size (H x W x L) | 91 x 81 x 262 mm (3.6 x 3.2 x 10.3 in) |
| Mounting | 2 x pair of tapped holes (1/4-20 thread) inner pair: 50.8 mm (2.0 in) center spread outer pair: 73.7 mm (2.9 in) center spread |
| Rear fittings (-20 models) | 1x cable diameter: 3.5 to 8.0 mm (0.14 to 0.32 in) 2x cable diameter: 5.8 to 10 mm (0.23 to 0.39 in) |
| Rear connectors (-50 models) | 1x 4-pin (power) 1x BNC (hybrid analog video) |
| Bottom fittings (-20 models) | 2x cable diameter: 4.5 to 7.9 mm (0.18 to 0.31 in) |

| Power Housing |
| --- |
| Power input (230 VAC) | freq. 50 Hz consumption 45 W fuse 2 A |
| Power input (24 VAC) | freq. 60 Hz consumption 45 W fuse 4 A |

| Environmental |
| --- |
| Operating Temperature | -40°C to +50°C (-40°F to 122°F) |
| Storage Temperature | -40°C to +70°C (-40°F to +158°F) |
| Operating Humidity | 20% to 93% RH |
| Storage Humidity | up to 98% RH |
| Enclosure protection | IP66, NEMA 4X |

| Camera Sensor |
| --- |
| Type | 960H, 1/3" DS CCD, sensor resolution 720TVL, WDR dual shutter |
| System | PAL or NTSC |
| Total pixels (H x V) | 1020 x 596 (PAL) 1020 x 508 (NTSC) |
| Effective pixels (H x V) | 976 x 582 (PAL) 976 x 494 (NTSC) |

| Video performance |
| --- |
| Sensitivity – (3200K, reflectivity 89%, F1.2) |
|  | Full video (100 IRE) | Usable picture (50 IRE) | Usable picture (30 IRE) |
| Color | 0.5 lx (0.0465 fc) | 0.09 lx (0.00837 fc) | 0.04 lx (0.00372 fc) |
| Color + SensUp 10x | 0.05 lx (0.00465 fc) | 0.009 lx (0.000837 fc) | 0.004 l (0.000372 fc) |
| Monochrome | 0.2 lx (0.0186 fc) | 0.04 lx (0.00372 fc) | 0.02 lx (0.00186 fc) |
| Monochrome SensUp 10x | 0.02 lx (0.00186 fc) | 0.004 lx (0.000372 fc) | 0.002 lx (0.000186 fc) |

| Video functions |
| --- |
| Signal-to-Noise Ratio | >54 dB |
| Video Output | Composite video 1 Vpp, 75 ohm |
| Synchronization | Internal, Line Lock |
| Shutter | Auto (1/50 [1/60] to 1/100000) selectable, fixed, flickerless, default |
| Sensitivity Up | Adjustable from Off up to 10x |
| Day/Night | Color, Mono, Auto |
| Dynamic Engine | XF-Dynamic, HDR, Smart BLC |
| Dynamic Range | 94 dB (WDR) |
| Dynamic Noise Reduction | 2D-NR, 3D-NR |
| AGC | AGC On or Off (0 – 40 dB) selectable |
| Smart BLC | On/Off |
| Peak White Invert | On/Off |
| White Balance | ATW Indoor, ATW Outdoor, ATW hold and Manual |
| Contrast Enhancement | Low, Medium, High |
| Sharpness | Sharpness enhancement level selectable |
| Alarm Output | VMD or Bilinx |
| Alarm Input (TTL) | Profile switching, +3.3 V nominal, +40 VDC max. |
| Alarm Output Relay | 30 VAC or +40 VDC, Max 0.5 A continuous, 10 VA |
| Cable Compensation | Up to 1000 m (3000 ft) coax without external amplifiers (automatic set-up in combination with Bilinx coaxial communication) |
| Camera ID | 17 character editable string, position selectable |
| Test Pattern Generator | Color bar, Raster, Impulse, Cross Impulse, Cross hatch, |
| Modes | 6 preset programmable modes |
| Remote Control | Bilinx coaxial bi-directional communication |
| Video Motion Detection | 4 areas, fully programmable |
| Privacy Masking | 15 independent areas, fully programmable |
| E-Zoom | Up to 16x |
| Digital Image Stabilizer | On/Off |
| Controls | OSD with soft-key operation |
| OSD Language | English, French, German, Spanish, Portuguese, Simplified Chinese, Russian |

| Lens | LVF-5000C-D2811 Varifocal Lens | LVF-5000C-D0550 Varifocal Lens |
| --- | --- | --- |
| Focal length | 2.8 – 11 mm | 5.0 – 50 mm |
| Iris range | F1.4 - 360 | F1.6 - 360 |
| Min object distance | 0.3 m (1.0 ft) | 0.3 m (1.0 ft) |
| Lens mount | CS | CS |
| Angle of view (HxV) | W: 97.4 x 72.4 T: 26.2 x 19.7 | W: 51.2 x 39.4 T: 5.3 x 4.1 |
| MTF on-axis (lp/mm) | >250 >223 (IR) | >165 >144 (IR) |
| MTF off-axis (lp/mm) | >145 >131 (IR) | >81 >30 (IR) |
| Iris control | 4-pin, DC control | 4-pin, DC control |
| Focus control | manual | manual |
| Zoom control | manual | manual |
| IR corrected | yes | yes |

| Mount LTC 9215/00 |
| --- |
| Length | 300 mm (12 in) |
| Maximum Load | 9 kg (20 lb) |
| Mounting Head | Adjustable 360° pan, 180° tilt |
| Finish | Light gray |
| Approx. Weight | 0.4 kg (0.9 lb) |
| Mounting | 2 x tapped holes Thread: 1/4-20 73.7 mm (2.9 in) center spread |

  - ACCESSORIES

None

- – EXECUTION

  - EXAMINATION

    - Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

    - Do not begin installation until unacceptable conditions are corrected.

  - PREPARATION

    - Protect devices from damage during construction.

  - INSTALLATION

    - Install devices in accordance with manufacturer’s instruction at locations indicated on the floor drawings plans.

    - Ensure selected location is secure and offers protection from accidental damage.

    - Location must provide reasonable temperature and humidity conditions, free from sources of electrical and electromagnetic interference.

  - FIELD QUALITY CONTROL

    - Test snugness of mounting screws of all installed equipment.

    - Test proper operation of all video system devices.

    - Determine and report all problems to the manufacturer’s customer service department.

  - ADJUSTING

    - Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

    - Make any adjustment of camera settings to comply with specific customer’s need.

  - DEMONSTRATION

    - Demonstrate at final inspection that video management system and devices function properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.