### Praesideo Call Station Keypad Module PRS-CSKPM

### Architects’ and Engineers’ Specifications

The call station keypad module shall provide connections for switches and indicators to enable an installer to create custom build call station panels in combination with a call station module. It shall have a serial digital interface to connect to a (remote) call station or (remote) call station module, with loop through facilities for additional keypads or keypad modules.

The keypad shall provide connections for 8 switches (keys) and 16 LEDs, which can be configured via the network to provide various functions for the call station, to which it is connected.

The configuration shall allow for selection and control functions to be programmed for each switch.

It shall be possible to configure the switches for different modes of operation, such as momentary or toggle operation. Each switch shall have 2 complementary LEDs for status indication.

The keypad based on the module shall get its power from the call station it is connected to.

The unit shall be able to operate at a maximum operating temperature of 55°C.

The call station keypad module shall be certified by an independent Notified Body for compliancy to the standards EN 60849, EN 54-16 and ISO 7240-16 for emergency sound systems.

The call station keypad module shall be a Praesideo PRS-CSKPM, manufactured by Bosch Security Systems.