August 2011

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5600 JB Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Robert Bosch (SEA) Pte Ltd, Security Systems 11 Bishan Street 21 Singapore 573943 Phone: +65 6571 2600 Fax: +65 6571 2698 apr.securitysystems@bosch.com www.boschsecurity.com |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 29

VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

BOSCH EX12LED 3D DIFFUSER INFRARED ILLUMINATOR

- – GENERAL

  - SUMMARY

    - Section Includes

      - Video Surveillance Remote Devices and Sensors

    - Related Sections

      - Section [26 55 53 – Special Purpose Lighting – Security Lighting].

      - Section [28 23 13 – Video Surveillance Control and Management Systems].

      - Section [28 23 16 – Video Surveillance Monitoring and Supervisory Interfaces].

      - Section [28 23 23 – Video Surveillance Systems Infrastructure].

**********Specifier’s note: Include those standards referenced elsewhere in this SECTION.

  - REFERENCES

    - Canadian Standards Association (CSA)

      - CSA E60065 Audio, Video and Similar Electronic Apparatus - Safety Requirements.

    - European Norm

      - EN 50130-4 Alarm Systems - Electromagnetic Compatibility - Product Family Standard: Immunity Requirements For Components Of Fire, Intruder And Social Alarm Systems.

      - EN 55022 class A (CE) – Information Technology Equipment – Radio Disturbance Characteristics – Limits and Methods of Measurement for Emission.

      - EN 60065 Audio, video and similar electronic apparatus. Safety requirements.

    - Federal Communications Commission (FCC) (www.fcc.gov)

      - FCC CFR 47 part 15 class B – Telecommunications – Radio Frequency Devices – Digital Device Emission

    - International Organization for Standardization (ISO)

      - 9001 – Quality System

    - Underwriters Laboratories, Inc. (UL) (www.ul.com)

      - UL 60065 Audio, Video and Similar Electronic Apparatus - Safety Requirements.

  - SYSTEM DESCRIPTION

    - Video Surveillance Remote Devices

      - Bosch EX12LED 3D Diffuser Infrared Illuminator

    - Performance Requirements

      - The infrared illuminator shall use 3D diffuser even-illumination technology.

      - The infrared illuminator shall 850 nm (semi-covert) or 940 nm (covert) options.

      - The infrared illuminator shall offer adjustable infrared intensity.

      - The infrared illuminator shall have a maximum range of 30 m (100 ft).

      - The infrared illuminator shall offer a photocell control with an adjustable day/night switch point.

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00].

    - Product Data:

      - Manufacturer’s data, user and installation manuals for all equipment and software programs including computer equipment and other equipment required for complete video management system.

    - Shop Drawings; include

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals

      - User manual.

      - Parts list.

      - System device locations on architectural floor plans.

      - Wiring and connection diagram.

      - Maintenance requirements.

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design Video Surveillance Devices.

      - Manufacturer’s quality system: Registered to ISO 9001 Quality Standard.

    - Video Surveillance System

      - Listed by [UL] [EN] [FCC] specifically for the required loads.  Provide evidence of compliance upon request.

    - Installer:

      - Minimum of [2] years experience installing Video IP Surveillance System.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section [01 60 00].

    - Deliver materials in manufacture’s original, unopened, undamaged containers; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions.

    - Bosch provides off-the-shelf availability for our top selling products and same-day or 24-hour shipping.

  - WARRANTY

    - Provide manufacturer’s warranty covering [5] years for replacement and repair of defective equipment.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m EST. via phone and e-mail.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5600 JB Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

[Bosch Security Systems Pte Ltd

Robert Bosch (SEA) Pte Ltd, Security Systems

11 Bishan Street 21

Singapore 573943

Phone: +65 6571 2600

Fax: +65 6571 2698

apr.securitysystems@bosch.com

www.boschsecurity.com]

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

**********Specifier’s note: Select Illuminator based on project requirement.

  - BOSCH AEGIS UFLED INTELLIGENT-IR ILLUMINATOR [EX12LED-3BD-8M] 
[EX12LED-3BD-8W] [EX12LED-3BD-9M] [EX12LED-3BD-9W]

    - General Characteristics:

      - The infrared illuminator shall be LED type.

      - The infrared illuminator shall be 74W x 70D x 70H mm (2.9 x 2.8 x 2.8 in.), weigh no more than 454g (1.0 lb) and be robust.

      - The infrared illuminator shall operate with high efficiency.

      - The infrared illuminator shall operate with high reliability.

      - The infrared illuminator shall operate in harsh weather conditions.

      - The infrared illuminator shall have been rigorously tested and proven for use by the manufacturer.

    - Performance

      - The infrared illuminator shall provide infrared illumination suitable for maximum range up to 30 m (100 ft) when used in combination with appropriate high-sensitivity analog and IP cameras and lenses.

      - The infrared illuminator shall provide the performance under zero lux conditions.

      - The infrared illuminator shall be available in wavelengths of 850 nm or 940 nm.

      - The infrared illuminator shall be available in beam patterns of 30º (medium) or 60º (wide).

      - The infrared illuminator shall have a high-efficiency infrared array comprised of 3 LEDs.

      - The infrared illuminator shall have diffused illumination using 3D Diffuser technology.

      - The infrared illuminator shall enable increased surveillance range, wider beam patterns, and evenly illuminated nighttime surveillance with 3D Diffuser technology.

      - The infrared illuminator shall eliminate hotspots in the foreground and underexposed backgrounds with 3D Diffuser technology.

      - The infrared illuminator shall use a sensitivity-adjustable photocell.

      - The infrared illuminator shall have photocell-controlled on/off switching.

      - The infrared illuminator shall have intensity adjustable output.

      - The infrared illuminator shall dissipate thermal energy through an integral heat sink.

      - The infrared illuminator shall operate independently of any cooling fan or similar device, either internal or external.

      - The infrared illuminator shall have a solid state design without any moving mechanical parts.

      - The infrared illuminator shall offset the bandwidth requirements for IP cameras in low-light applications.

    - Performance Ranges

      - The infrared illuminator shall offer the following performance ranges:

        - [EX12LED-3BD-8W

          - LED Type: 850 nm

          - LED Beam Angle: 60° wide

          - Range: 15 m (50 ft)

          - Horizontal Field of View: 17 m (56 ft)]

        - [EX12LED-3BD-8M

          - LED Type: 850 nm

          - LED Beam Angle: 30° medium

          - Range: 30 m (100 ft)

          - Horizontal Field of View: 16 m (53 ft)]

        - [EX12LED-3BD-9W

          - LED Type: 940 nm

          - LED Beam Angle: 60° wide

          - Range: 7 m (23 ft)

          - Horizontal Field of View: 8 m (26 ft)]

        - [EX12LED-3BD-9M

          - LED Type: 940 nm

          - LED Beam Angle: 30° medium

          - Range: 15 m (50 ft)

          - Horizontal Field of View: 8 m (26 ft)]

    - Construction

      - The infrared illuminator shall be made of anodized CNC aluminum.

      - The infrared illuminator shall have a front window made of optical acrylic for discreet operation.

      - The infrared illuminator shall have a black finish.

      - The infrared illuminator shall be compact, robust and sealed for performance under all weather conditions.

      - The infrared illuminator shall operate independently of any cooling fan or similar device, either internal or external.

      - The infrared illuminator shall dissipate thermal energy through an integral heat sink.

      - The infrared illuminator shall have a solid state design without any moving mechanical parts.

      - The infrared illuminator shall weigh no more than 454 g (1.0 lb).

      - The infrared illuminator shall have dimensions (WxDxH) of 74 x 70 x 70 mm 
(2.9 x 2.8 x 2.8 in.)

      - .The infrared illuminator shall be supplied with a U-bracket for easy mounting and adjustment.

    - Power Requirements

      - The infrared illuminator shall be an energy-efficient unit, consuming 9 W.

      - The infrared illuminator shall have a sensitivity adjustable photocell for automatic on/off operation.

      - The infrared illuminator shall be capable of accepting direct 12 to 24 VDC or 24 VAC power.

    - Environmental

      - The infrared illuminator shall operate in temperatures ranging from 
-50ºC to +60ºC (-58ºF to 140ºF).

      - The infrared illuminator shall be environmentally sealed to NEMA 4X standards.

    - Specifications:

      - LED

        - LED Type:

          - [850 nm]

          - [940 nm]

        - LED Beam Angle

          - [30°]

          - [60°]

        - IR Control: Adjustable IR intensity

        - Day/Night Switch: Photocell, sensitivity adjustable

      - Electrical

        - Power Supply: 12-24 VDC or 24 VAC

        - Power Draw:9 W

      - Mechanical

        - Housing: Aluminum, black

        - Front Window: Optical Lexan

        - Mount: 1/4-in.-20 thread at bottom and rear

        - U-bracket: Standard with 1/4-in.-20 bolt included

        - Dimensions (WxDxH): 74 x 70 x 70 mm (2.9 x 2.8 x 2.8 in.)

        - Weight: 454 g (1.0 lb)

      - Environmental

        - Operation Temperature Range: -50°C to +60°C (-58°F to +140°F)

        - Certification: NEMA 4X

  - ACCESSORIES

    - UPA-2420-50, 220 VAC, 50 Hz Power Supply

    - UPA-2420-60, 120 VAC, 60 Hz Power Supply

    - PSU-124-DC050 50 W Single-Channel Power Supply

    - EXMB.020B L-bracket

- – EXECUTION

  - EXAMINATION

    - Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

    - Do not begin installation until unacceptable conditions are corrected.

  - PREPARATION

    - Protect devices from damage during construction.

  - INSTALLATION

    - Install devices in accordance with manufacturer’s instruction at locations indicated on the floor drawings plans.

    - Ensure selected location is secure and offers protection from accidental damage.

  - FIELD QUALITY CONTROL

    - Test mounting fasteners for proper tightness per the installation guide.

    - Test proper operation of all video system devices.

    - Determine and report all problems to the manufacturer’s customer service department.

  - ADJUSTING

    - Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

    - Make any adjustment of camera settings to comply with specific customer’s need.

  - DEMOSTRATION

    - Demonstrate at final inspection that video management system and devices function properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.