Architect’s Specifications

The synoptic microphone and voting software provides a range of conference facilities including automatic seat assignment, synoptic microphone monitoring and control, and voting management. The software runs on a PC with a mouse or touch-screen, it has an intuitive graphic user interface suitable for touch screen operation with on-screen help in most major languages. The user interface has a graphical representation of the conference venue - a connected device is automatically recognized and an icon is created for it on the on-screen room layout. The icons display information about device status and can be used by the operator to select individual devices for remote control functions. Icons are specially designed so they can be identified by persons with the visual disability of color blindness. Other functions:

- operator is alerted if a device is disconnected from the system

- names can be assigned to microphone icons (the positions of the icons on the room layout can be changed using the standard windows ‘drag & drop’)

- microphone control to observe and switch each microphone on and off, or place in the ‘request to speak’ list

- system operator can request delegates to vote, as well as start and stop voting sessions. Final vote results can be automatically printed or exported to a file; the software can be configured to send real-time voting information to Microsoft PowerPoint® for displaying in different formats. Individual voting results can be shown in different colors according to votes cast.

- remaining battery capacity and signal strength is shown for each wireless discussion unit.

Manufacturer:	Bosch Security Systems

Type:		DCN-SWSMV