### Praesideo PC Call Station Client PRS-CSC

### Architects’ and Engineers’ Specifications

The PC call station client is a client of the PC call server and shall be used with the PC call server. It shall run on a PC under Windows. It shall be possible to run multiple PC call station clients concurrently connected to the same PC call server.

The PC call station client shall provide a graphical user interface to the operator, where the operator can select predefined calls, add or remove zones from that predefined call by clicking on zone icons in a graphical system layout, and then start, stop and/or abort this call. Multiple calls can be active simultaneously from the same

client. Zone icon appearance shall represent the status of each zone.

BGM source selection and volume shall be selectable per zone and the actual source and volume setting shall be indicated in the zone icon.

It shall be possible to customize the user interface of the call station client by modifying the library of zone icons for appearance and color, adding a customer logo to the user interface screen and changing the user interface language.

The PC call station client shall be a Praesideo PRS-CSC, manufactured by Bosch Security Systems.