### Praesideo Basic Power Amplifier PRS-2B250

### Architects’ and Engineers’ Specifications

The 2-channel amplifier shall provide connection facilities to a multi-channel interface unit, which in turn shall be connected to an audio and control network, based on fiber optical hybrid cabling, capable of redundant loop operation. Via the multi-channel interface, the amplifier shall be able to receive audio and operational control signals from the network and report its status to the system controller.

The amplifier shall contain 2 analog audio input, one for each channel, supporting line level with gain control by a preset potentiometer, for direct connection to an auxiliary audio source. The amplifier shall have a priority circuit that will overrule a directly connected audio source when audio from the network is routed to this amplifier channel.

The power amplifier shall be a 2-channel power amplifier with a rated output power of 250 Wrms per channel. It shall be able to deliver rated power at a maximum operating temperature of 55°C to accommodate high density rack mounting. The amplifier shall use highly efficient class-D switched mode technology for low power consumption. The amplifier shall have constant voltage outputs for 70 V and 100 V, typical for public address loudspeaker systems.

The amplifier shall have group A and group B loudspeaker outputs per amplifier channel, supporting individual overload protection per group. In case of amplifier overload, the amplifier shall diagnose the group A and group B outputs to identify the overloaded group and only disconnect that group, keeping the loudspeakers on the other group operational. The amplifier shall support Class A loop operation per channel with a loudspeaker loop connected between the group A and group B outputs.

For each channel, the loudspeaker connections shall be on a detachable screw terminal with safety insulation and shall be transformer isolated and floating with respect to ground.

For each channel, the amplifier, in co-operation with the connected multi-channel interface, shall have a ground leakage detector to detect insulation failure of the loudspeaker wiring to warn against hazardous situations. The amplifier shall be protected against overheat, overload and short circuits.

The amplifier shall have a supervision system to monitor its operation conditions and the connected load. For each channel separately, the amplifier shall have a built-in relay for automatically connecting the loudspeaker load to a spare amplifier in case of amplifier failure. The amplifier channels shall operate completely independent of each other and allow one channel of the amplifier to be a spare amplifier for the other channel.

The amplifier shall support loudspeaker line and individual loudspeaker supervision using communication to end-of-line supervision units or loudspeaker supervision units. Power supply to and communication with these supervision units shall be via the 2-conductor loudspeaker cable itself, without the need for additional conductors or shielded wiring.

The amplifier shall have a high-efficiency switched mode power supply for mains operation and a 48 V battery input for backup purposes with automatic switchover.

The amplifier shall be able to monitor the mains power and the battery power to the amplifier. The amplifier shall have a configurable sleep mode to save battery power in case of mains power failure, with automatic wake-up in case a priority call must be made.

The amplifier shall have indicator LEDs on the front panel for mains and battery status, amplifier output level per channel and fault status per channel. Fault conditions shall also be reported by the amplifier, in co-operation with the connected multi-channel interface, to a network connected system controller for logging purposes.

The amplifier shall be certified by an independent test agency, such as the German TÜV, for compliancy to the standards EN 60849 and EN 54-16 for emergency sound systems.

The amplifier cabinet shall be 19”-wide and 2U-high for easy rack mounting without the need for free rack space between units.

The amplifier shall be a Praesideo PRS-2B250, manufactured by Bosch Security Systems.