### Praesideo Non-addressable Fiber Interface PRS-FINNA

### Architects’ and Engineers’ Specifications

The non-addressable fiber interface shall have a network interface for plastic fiber optical hybrid cabling and a network interface for multi-mode glass fiber optical cabling. The fiber interface shall act as a bi-directional converter with data refreshing between plastic fiber and glass fiber with the purpose of extending the distance between network nodes to more than can be covered with plastic fiber, using glass fiber instead.

The fiber interface shall be capable of redundant loop operation, supporting digital audio and control signals.

The fiber interface shall be powered from the hybrid network for easy installation, but it shall also be possible to power the fiber interface and connected units from an external power supply. The fiber interface shall have a power status LED and a network status LED for diagnostic purposes.

The non-addressable fiber interface shall not have an address on the network in order not to occupy a node-position and limit the network size. As a consequence the unit will be invisible for the controller of the network, making fault reporting for logging not possible, but the fiber interface shall pass through faults from connected units.

The unit shall be able to operate at a mximum operating temperature of 45°C. With the unit a bracket shall be supplied for easy mounting.

The fiber interface shall be certified by an independent test agency, such as the German TÜV, for compliancy to the standards EN 60849 and EN 54-16 for emergency sound systems.

The fiber interface shall be a Praesideo PRS-FINNA, manufactured by Bosch Security Systems.