### PLENA 6-zone call station LBB1946/00

### Architects’ and Engineers’ Specifications

The call station shall have a metal base for stability, a flexible microphone stem and a uni-directional condenser microphone.

It shall be part of a sound amplification system, such that there is a direct connection between the call station and a matching amplifier, or between the call station and another call station in the same system. The call station shall have a 5m interconnection cable terminated with a lockable 8-pin DIN connector. It shall have a loopthrough connector to provide connection possibilities for subsequent call stations.

The design of the call station shall allow for both flush mounting in desktops and for tabletop use.

The call station shall provide facilities to make calls to up to six selected zones in a PA system and also have single button all-call selection. Selected zones shall be indicated with amber LEDs on the call station, and two additional LEDs shall give visible feedback on the active state of the microphone and the system. A green LED shall indicate microphone on or chime active (flashing LED); amber shall indicate that the system is occupied by a source with a higher priority or operation error (flashing LED).

It shall be possible to insert a user editable label into the call station to show the names of the zones through transparent windows.

The call station shall have selectable gain, a selectable speech filter and a limiter for improved intelligibility in case the speaker moves in front of the microphone.

The call station shall provide a balanced line level output to allow for positioning up to 450m away from the amplifier, using CAT-5 extension cables.

In combination with a matching amplifier, dipswitches on the bottom of the call station shall be able to select different pre- and post-announcement chimes, as well as the priority level.

The unit shall have an operating temperature range of –10 to +55(C. The unit shall comply with EN55103-1 and EN55103-2 for EMC emission and immunity.

The call station shall be a Plena model LBB1946/00, manufactured by Bosch Security Systems.

| 3122 475 21412 en | 03-40 | © 2003 Robert Bosch GmbH Data subject to change without notice. |
| --- | --- | --- |