March 2019

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5617 BA Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Robert Bosch (SEA) Pte Ltd, Security Systems 11 Bishan Street 21 Singapore 573943 Phone: +65 6571 2808 Fax: +65 6571 2699 apr.securitysystems@bosch.com www.boschsecurity.asia |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 29

VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

Bosch FLEXIDOME IP indoor 5000i (IR) camera

- – GENERAL

  - SUMMARY

    - Section Includes

      - Video Surveillance Remote Devices.

    - Related Sections

      - Section [28 23 13 – Video Surveillance Control and Management Systems].

      - Section [28 23 16 – Video Surveillance Monitoring and Supervisory Interfaces].

      - Section [28 23 19 – Digital Video Recorders and Analog Recording Devices].

      - Section [28 23 23 – Video Surveillance Systems Infrastructure].

**********Specifier’s note: Include those standards referenced elsewhere in this SECTION.

  - REFERENCES

    - Australia and New Zealand Standards

      - AS/NZS CISPR 22 Information technology equipment - Radio disturbance characteristics - Limits and methods of measurement

      - Conforms to C-tick standards

    - Canadian Standards Association (CSA)

      - CAN/CSA-C22.2 No. 60950-1 Information Technology Equipment - Safety - Part 1: General Requirements (Bi-National standard, with UL 60950-1)

      - CAN/CSA-C22.2 No. 60950-22 Information Technology Equipment - Safety - Part 22: Equipment to be Installed Outdoors (Bi-National standard, with UL 60950-22)

      - Conforms to cUL standards

    - European Norm

      - EN 50121-4:2006 Railway Applications - Electromagnetic Compatibility - Part 4: Emission And Immunity Of The Signaling And Telecommunications Apparatus

      - EMC directive 2004/108/EC

      - EN 50130-4:1995+A1:1998+A2:2003 (CE) Alarm Systems, Part 4 – Electromagnetic Compatibility – Product Family Standard: Immunity Requirements for Components of Fire, Intruder and Social Alarm Systems.

      - EN 50130-5: Alarm Systems, Part 5 – Environmental Test Methods (corresponds with VDE 0830 parts 1-5)

      - EN 50132-5-2: Alarm systems - CCTV surveillance systems for use in security applications - Part 5-2: IP Video Transmission Protocols

      - EN 55032, Class B – Information Technology Equipment – Radio Disturbance Characteristics – Limits and Methods of Measurement for Emission

      - EN 55024 Information technology equipment. Immunity characteristics. Limits and methods of measurement

      - EN60950-1 – Safety of information technology equipment (IT Equipment)

      - CE Declaration of Conformity

      - CB scheme

    - Federal Communications Commission (FCC) (www.fcc.gov)

      - FCC CFR 47 part 15; subpart B, Class B Digital Devices

    - Industry Canada

      - ICES-003 Class B Spectrum Management and Telecommunications Policy Interference-Causing Equipment Standard

    - International Electrotechnical Commission (IEC):

      - IEC 62676-2-3: Video surveillance systems for use in security applications – Part 2-3: Video transmission protocols – IP interoperability implementation based on WEB services.

      - IEC 62471 (IR version): Photobiological safety of lamps and lamp systems.

    - International Organization for Standardization (ISO)

      - 9001: Quality System

    - Underwriters Laboratories, Inc. (UL) (www.ul.com)

      - UL 60950-1 UL Standard for Safety of Information Technology Equipment.

      - UL 60950-22 Information Technology Equipment – Safety - Part 22: Equipment to be installed outdoors

    - Voluntary Control Council for Interference (VCCI)

      - VCCI J55022 V2/V3

    - EurAsion Standards

      - EurAsian Conformity (EAC, Russian: Евразийское соответствие) - The products conforms to all technical regulations of the Eurasian Customs Union assessment procedures. It can be serviced in the territory of all Customs Union member countries: Russia, Belarus, Armenia, Kazakhstan and Kyrgyzstan

  - DEFINITIONS

    - Sensitivity: refers to the minimum level of light the sensor needs to generate an acceptable video picture, and is measured in lux.

    - Day/Night (infrared sensitive): The camera has normal color operation in situations where there is sufficient illumination (day conditions), but when there is little light available (night conditions) the sensitivity is increased by removing the infrared cut-off filter to provide a monochrome image.

    - iDNR (intelligent Dynamic Noise Reduction): The Intelligent Dynamic Noise Reduction applies temporal noise filtering when no motion is detected. The filtering reduces the noise in the image and this makes the encoder step more effective.

  - SYSTEM DESCRIPTION

    - Video Surveillance Remote Devices

      - NDI-5503-A FLEXIDOME IP indoor 5000i 5MP camera

      - NDI-5503-AL FLEXIDOME IP indoor 5000i 5MP IR camera

    - Performance Requirements

      - Complete indoor network video surveillance system inside a dome camera.

      - 5MP resolution.

      - Built-in active infrared illuminator (NDI-5503-AL only).

      - Built-in Essential Video Analytics to trigger relevant alerts and quickly retrieve data.

      - High Dynamic Range (HDR) to see details in bright and dark areas simultaneously.

      - Intelligent Dynamic Noise Reduction (iDNR) technology.

      - Intelligent streaming technology for reduced bitrates

      - H.264 and H.265 encoding

      - Automatic varifocal 3 to 10 mm, DC Iris fixed board-mounted lens.

      - True day/night function.

      - Quad-streaming IP video

      - Micro SDHC/SDXC card slot for edge recording up to 2 TB.

      - ONVIF conformant.

      - +12 VDC, +24 VAC and Power over Ethernet (IEEE 802.3af compliant).

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00].

    - Product Data:

      - Manufacturer’s data, user and installation manuals for all equipment and software programs including computer equipment and other equipment required for complete video management system.

    - Shop Drawings; include

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals

      - User manual.

      - Parts list.

      - System device locations on architectural floor plans.

      - Wiring and connection diagram.

      - Maintenance requirements.

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design Video Surveillance Devices.

      - Manufacturer’s quality system: Registered to ISO 9001 Quality Standard.

    - Video Surveillance System

      - Listed by [UL] [EN] [FCC] specifically for the required loads.  Provide evidence of compliance upon request.

    - Installer:

      - Minimum of [5] years experience installing Video Surveillance Systems.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section [01 60 00].

    - Deliver materials in manufacture’s original, unopened, undamaged containers; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions.

    - Bosch provides off-the-shelf availability for our top selling products and same-day or 24-hour shipping.

  - WARRANTY

    - Provide manufacturer’s warranty covering [3] years for replacement and repair of defective equipment.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m. via phone and e-mail.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5617 BA Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

[Robert Bosch (SEA) Pte Ltd, Security Systems

11 Bishan Street 21

Singapore 573943

Phone: +65 6571 2808

Fax: +65 6571 2699

apr.securitysystems@bosch.com

www.boschsecurity.com]

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

**********Specifier’s note: Select Camera System Series based on project requirement.

  - FLEXIDOME IP indoor 5000i (IR) [NDI-5503-A(L)]

    - General Characteristics:

      - The camera shall be capable of operating in an indoor environment.

      - The camera shall have a 5MP sensor

      - The camera shall offer tamper detection and Essential Video Analytics.

      - The camera shall offer two-way full duplex audio communication.

      - The camera shall have a built-in active infrared illuminator (NDI-5503-AL only)

      - The camera shall provide a CVBS (PAL/NTSC), 1 Vpp, BNC, 75 Ohm analog output that allows hybrid video output.

      - The camera shall utilize Intelligent Dynamic Noise Reduction (iDNR) technology to reduce the bitrate and storage requirements by removing noise artifacts

      - The camera shall offer Intelligent streaming possibilities.

      - The camera shall have an gyrosensor / accelerometer

      - The camera shall provide eight independent, fully programmable privacy mask areas.

      - The camera shall be easy to install.

    - Imaging Requirements

      - The camera shall offer a 1/2.9-inch CMOS image sensor.

      - The camera shall produce a video resolution of 3072x1728 pixels (MP 5MP) at 30 fps with a 16:9 aspect ratio.

      - The camera shall produce a video resolution of 2688x1512 pixels (MP 4MP) at 30 fps with a 16:9 aspect ratio.

      - The camera shall produce a video resolution of 2304x1296 pixels (MP 3MP) at 30 fps with a 16:9 aspect ratio.

      - The camera shall produce a resolution of 1920 x 1080 pixels (HD 1080p) at 30 fps with a 16:9 aspect ratio.

      - The camera shall offer an upright mode

      - The camera shall be fitted with a board-mounted fixed varifocal 3 to 10 mm, DC Iris, F1.3 lens with a lens view angle of:

        - 29° - 92° (Horizontal)

        - 18° - 50° (Vertical).

      - The camera shall have a wide dynamic range of 120 dB HDR.

      - The camera shall have high sensitivity color (0.24 lx) and in monochrome (0.03 lx). The camera shall offer a minimum sensitivity of 0.0 lx in IR mode (NDI-5503-AL only).

      - The camera automatic electronic shutter shall offer a shutter speed of 1/30 (1/25) to 1/15000.

      - The camera shall be capable of capturing and storing images using the following compression standards:

        - H.265 MP

        - H.264 MP

        - M-JPEG

    - Network Video

      - The camera shall provide direct network connection using H.265, H.264 and M-JPEG compression and bandwidth throttling to efficiently manage bandwidth and storage requirements while delivering outstanding image quality.

      - The camera shall allow full camera control and configuration capabilities over the network.

      - The camera shall deliver video, at rates up to 30 images per second, via TCP/IP over a 10/100 Base-T, auto-sensing, half/full duplex, RJ45 Ethernet connection.

      - The camera shall support AutoMDIX.

      - The camera shall conform to the ONVIF Profile S and G standard.

      - The camera shall conform to protocols: IPv4, IPv6, UDP, TCP, HTTP, HTTPS, RTP/RTCP, IGMP V2/V3, ICMP, ICMPv6, RTSP, FTP, Telnet, ARP, DHCP, SNTP, SNMP (V1, MIB-II), 802.1x, DNS, DNSv6, DDNS, SMTP, iSCSI, UPnP (SSDP), DiffServ (QoS), LLDP, SOAP, Dropbox, CHAP, Digest Authentication.

    - Audio

      - The camera shall have line in and line out jack connectors for two-way, full duplex audio communication with audio compression AAC, G.711, L16 (live and recording).

    - Night Vision (Infrared) (NDI-5503-AL only).

      - The camera shall have a 10 LED high efficiency array (850 nm) for effective night vision up to 30 m (98 ft).

    - Control

      - The camera shall be configured via a web browser or PC surveillance software.

    - Connectors

      - The camera shall have one RJ-45 for Ethernet.

      - The camera shall have one analog video out BNC connector for installation only.

      - The camera shall have short or DC 5V activation alarm input.

      - The camera shall have one relay out (input rating maximum 1 A, 24 VAC/VDC).

      - The camera shall have one line in jack connector for audio input.

      - The camera shall have one line out jack connector for audio output

    - Electrical

      - The camera shall accept either +12 VDC, +24 VAC or Power over Ethernet (48 VDC nominal).

      - The camera shall conform to the IEEE 802.3af (802.3at Type 1) compliant Power over Ethernet network. Power level: Class 3.

      - The camera shall consume 7 W (max.).

    - Access Security

      - The camera shall offer three levels of password protection.

      - The camera shall support 802.1x authentication using a RADIUS (Remote Authentication Dial In User Service) server.

      - The camera shall store an SSL certificate for use with HTTPS.

    - Recording and Storage Management

      - The camera shall support iSCSI devices to allow video stream to be recorded directly to an iSCSI RAID array.

      - The camera shall support iSCSI storage targets to enable the camera to function as a conventional DVR.

      - The camera shall have an SD card slot that uses standard, off-the-shelf SD cards for local storage (up to 2TB).

      - The local storage feature shall be capable of storage for Automatic Network Replenishment (ANR).

      - Local Recording: Continuous recording, ring recording, alarm/events/schedule recording.

    - Alarm Handling Features:

      - The camera shall provide the capability on alarm to display up to a 31 character, programmable alarm message.

      - The camera shall provide email alarm messaging with optional JPEG posting.

    - Embedded Video Content Analysis

      - The camera shall be VCA enabled.

      - The camera shall be capable of processing and analyzing video within the camera itself, with no extra hardware required.

      - The camera shall be capable of detecting and sending alarms for abnormal events.

      - The camera shall allow users to set up to 10 separate profiles and switch profiles based on a day/night or holiday schedules.

      - The camera shall offer Essential Video Analytics that uses an Intelligent tracker to follow objects within the defined regions of interest.

    - Environmental

      - The camera shall operate in a -20°C to +50°C (-4°F to +122°F) temperature range.

      - The camera can be stored in a -30°C to +70°C (-22°F to +158°F) temperature range.

      - The camera can be operated/stored in 0% to 90% relative humidity (non-condensing).

    - Mechanical

      - The camera dimensions shall be:

        - Diameter 135 mm (5.32 in.)

        - Height 102 mm (4 in.).

      - The camera weight shall be 450 g (0.99 lb) approx.

      - The camera shall have 3-axis adjustment (pan/tilt/rotation), plus zoom.

      - The camera color is RAL 9003 and RAL 9017.

  - Accessories

    - Mounts

      - BUB-CLR-FDO Clear polycarbonate bubble for dome camera

      - BUB-TIN-FDO Tinted polycarbonate bubble for dome camera.

      - NDA-5031-PIP Interface plate to mount a camera to a pendant or pipe, white; for indoor use.

      - NDA-U-WMT Universal wall mount for dome cameras, white

      - NDA-U-PMT Universal pipe mount for dome cameras, 31 cm, white

      - NDA-U-PMAS Universal pole mount adapter, white; small.

      - NDA-U-PMTE Extension for universal pipe mount, 50 cm, white

      - NDA-U-PSMB Surface mount box (SMB) for wall mount or pipe mount.

      - NDA-FMT-DOME In-ceiling flush mounting kit for dome cameras (Ø157 mm)

      - NDA-ADT4S-MINDOME Surface mount box (Ø145 mm / Ø5.71 in) for dome cameras (use together with the appropriate dome adapter bracket).

      - NDA-U-CMT Universal corner mount, white

      - NDA-U-WMP Back plate for universal wall mount, corner mount and pole mount, white

      - LTC 9230/01 Flat Roof Mount Adapter for mounting a unit in an upright position on a flat surface.

      - NDA-U-WMT Universal wall mount for dome cameras, white

      - NDA-U-PMAL Universal pole mount adapter, white; large

    - Other

      - NBN-MCSMB-03M 0.3 m (1 ft) analog cable, SMB (female) to BNC (female) to connect camera to coaxial cable

      - NBN-MCSMB-30M 3 m (9 ft) analog cable, SMB (female) to BNC (male) to connect camera to monitor or DVR

      - UPA-1220-60 Power supply for camera. 100-240 VAC, 50/60 Hz In; 12 VDC, 1 A Out; regulated. Input connector: 2-prong, North American standard (non-polarized).

      - NPD-5001-POE Power-over-Ethernet midspan injector for use with PoE enabled cameras; 15.4 W, 1-port

      - NPD-5004-POE Power-over-Ethernet midspan injectors for use with PoE enabled cameras; 15.4 W, 4-ports

      - VJT-XTCXF High-performance video transcoder. H.264; CF card slot; ROI; max resolution 1080p; 2 channels

      - S1460 2.5 mm jack to BNC video connector cable. 1 m

- – EXECUTION

  - EXAMINATION

    - Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

    - Do not begin installation until unacceptable conditions are corrected.

  - PREPARATION

    - Protect devices from damage during construction.

  - INSTALLATION

    - Install devices in accordance with manufacturer’s instruction at locations indicated on the floor drawings plans.

    - Ensure selected location is secure and offers protection from accidental damage.

    - Location must provide reasonable temperature and humidity conditions, free from sources of electrical and electromagnetic interference.

  - FIELD QUALITY CONTROL

    - Test snugness of mounting screws of all installed equipment.

    - Test proper operation of all video system devices.

    - Determine and report all problems to the manufacturer’s customer service department.

  - ADJUSTING

    - Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

    - Make any adjustment of camera settings to comply with specific customer’s need.

  - DEMONSTRATION

    - Demonstrate at final inspection that video management system and devices function properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.