Software Release Notes

# Introduction

## Disclaimer of Warranty

Bosch Security Systems, Inc. makes no representations or warranties, either expressed or implied, by or with respect to anything in this document, and shall not be liable for any implied warranties of merchantability or fitness for a particular purpose or for any indirect, special or consequential damages.

## Purpose

The purpose of the Software Release Notes is to document is to communicate major new features and changes in this release of the Configuration Tool for Imaging Devices. It also documents component compatibility, workarounds, and any feature restrictions.

# Software Changes

- CTFID 3.14 supports the MIC Series 612 camera, with one caveat:

  - CTFID 3.14 does not display PTZ or Alarm data in the MIC Series 612 offline templates or in the Offline Configuration mode.

- CTFID 3.14 integrates a 64-bit driver for the USB Bilinx (VP-USB) device.  The driver has been successfully tested on 64- and 32-bit operating systems.

## Enhancements Implemented

The following ENHANCEMENTS have been resolved for this delivery.

Description

Implement Brightness interface for thermal camera

Implement thermal image mode

Add interface for second video channel (one for visible and one for thermal camera)

Implement Flat Field Correction (FFC) mode

Support MIC 612 orientation settings

Implement AGC Type menu item for thermal camera

Implement Show Test Pattern

## Defects Resolved

The following DEFECTS have been resolved for this delivery.

Description

Support for Fast Address of thermal cameras

Support Bilinx USB device drivers on 64-bit Windows 7 operating system.

Corrects the display of Stabilization setting check box.

Changed the MIC 550 Alarm rules input data for N.C. and N.O.

# Feature Restrictions

None.